## Slide 1
Understanding PFAS: Regulations, Sources, Chemistry, and Alternatives

## Slide 2: Agenda
Introductions & Housekeeping
Polling Question
Walter Brandl
Polling Question
Dr. Claire Sand
Questions & Answers

## Slide 3: Introductions & Housekeeping

## Slide 4: Housekeeping Reminders
You will receive a copy of the recorded presentation of today’s webinar within 1-2 days
Submit your questions in the Gotowebinar Control Panel

## Slide 5: Learning Objectives
Understand the chemistry and sources of PFAS
Understand the FDA’s regulatory requirements for PFAS
Learn the alternatives to PFAS, and how to prevent new PFAS

## Slide 6: Presenter Introductions
Walter Brandl
Regional Director of Chemistry
Mérieux NutriSciences
Dr. Claire Sand
Founder & Owner Packaging Technology & Research
Adjunct Professor, Michigan State University and CalPoly

## Slide 7: Polling Question:
Where does addressing PFAS rank on your priorities list for 2023?

## Slide 8: What is a PFA?
Reference: https://www.fda.gov/food/cfsan-constituent-updates/fda-makes-available-pfas-testing-results-first-survey-processed-foods
The per-and polyfluoroalkyl substances (PFAS) are a group of chemicals used to make fluoropolymer coatings and products that resist heat, oil, stains, grease, and water. Fluoropolymer coatings can be in a variety of products. These include clothing, furniture, adhesives, food packaging, heat-resistant non-stick cooking surfaces, and the insulation of electrical wire. Many PFAS, including perfluorooctane sulfonic acid (PFOS) and perfluorooctanoic acid (PFOA), are a concern because they:
do not break down in the environment,
can move through soils and contaminate drinking water sources,
build up (bioaccumulate) in fish and wildlife.
Source: Center for Disease Control and Prevention

## Slide 9: What is a PFA?
Reference: https://www.fda.gov/food/cfsan-constituent-updates/fda-makes-available-pfas-testing-results-first-survey-processed-foods
PFOS
PFOA

## Slide 10: US State Regulatory Activities - PFAs
Chemical hazards - PFAs
  Several states passed legislation or proposed bans of the use of perfluoroalkyl and polyfluoroalkyl substances (PFAS) in food and cosmetic packaging. (https://www.saferstates.com/toxic-chemicals/pfas/)
  EPA set health advisory for 4 PFAs in drinking water
  EPA lists PFAs on Toxic Release Inventory
  Class action law suits for companies claiming “natural” with PFAs

## Slide 11: US Drinking Water
Reference: https://oehha.ca.gov/proposition-65/proposition-65-list

## Slide 12: Canada
2018 Guidelines for Canadian Drinking Water Quality
  Set limits for 9 PFAs in drinking water
  Set limits for 11 PFAs in soil
  PFOs in fish tissue and bird eggs
2021 The Gazette published that the Government of Canada will:
  Continue to invest in research and monitoring on PFAS;
  Collect and examine information on PFAS to inform a class-based approach; and
  Review policy developments in other jurisdictions.

## Slide 13: Canada

## Slide 14: Canada

## Slide 15: European Union

## Slide 16: Analysis of PFAS
In choosing methods of analysis for PFAS we can go from the generic to the specific
    Total Fluorine
    Total Organic Fluorine
    PFAS groups or families
    targeted, individual specific PFAS compounds
    non-targeted, all-inclusive screen
In general as specificity increases, cost and time to result also increases

## Slide 17: Analysis of PFAS
Total Fluorine
  Sample pre-treatment is a combustion reaction to free up the fluorine from the matrix
  Free fluoride is water soluble
  Determination of fluoride can be made by selective ion electrode or ion chromatography

## Slide 18: Analysis of PFAS
Total Organic Fluorine
  Sample pre-treatment involves adsorption or extraction of the fluoride compounds, removal of inorganic fluoride
  Determination of fluoride can be made by selective ion electrode or ion chromatography

## Slide 19: Analysis of PFAS
Determination of PFAS groups or specific PFAS compounds
  Solvent extraction followed by solid phase clean-up.
  Addition of Internal Standards
  Determination by HPLC tandem mass spectrometer (LC-MSMS)
Sensitive and specific enough for current regulations (single digit ppt or lower)

## Slide 20: Analysis of PFAS
Detection of non-targeted PFAS compounds using Accurate Mass LC-MS
In general, qualitative analysis but quant can happen later
Allows for retrospective searches as the mass data can be stored for future analysis
Typically less sensitive than LC-MSMS
Can be used for confirmation of poorly resolved peaks

## Slide 21: Analysis of PFAS
Technique | Application | Comments
Total Fluoride | Screening packaging, firefighting foams | fast, 2-10 ppb in water,
Total Organic Fluorine | Screening of packaging, textiles, sediments | 
Targeted PFAS | foods, potable water, | regulatory compliant, sensitive and specific
non-targeted PFAS | risk assessment | 

## Slide 22: Polling Question:
In what areas are you addressing PFAS in 2023?

## Slide 23: Key Takeaways
PFAS regulations are creating stress
PFAS sources in food are from production, processing and packaging
Future Proof Packaging is needed to avoid the pitfalls of a fragmented approach
1
Industry has worked hard with a fragmented approach and alternatives to PFAS face roadblocks
2
3
4

## Slide 24: Selected Sources of PFAS in Packaging
Primary Packaging | Tertiary Packaging | Ingredients | Production Environment
1
2
3
4

## Slide 25: Selected Sources of PFAS Primary Packaging
Primary Packaging | Tertiary Packaging | Ingredients | Production Environment
Release Agents | Forming Polymers | Improved Barriers | Grease/ Oil Resistance
For Thermoforming, blowmolding | Wetting and leveling agents, emulsifiers, foaming agents, or dispersants | Fluorination of PE was approved in 1983 | Dry end coatings on paperboard and corrugated, and paper Lower the surface tension
 | Emulsifiers assist in producing Teflon examples include the use of PFOA | Now used during forming of in HPDE, PP, PET blowmolded, thermoformed containers | Wet end use on paperboard
 | Bond with functional groups such as acids and alcohols and/or take part in condensation polymerization of Nylon and PET | Primarily Polyﬂuoroalkyl substances | Coatings on hydroscopic polymers such as PLA, cellulose, starch, ethylenes, etc.
 |  | Polymers fluorinated with hexaﬂuoropropylene (HFP), tetraﬂuoroethylene (TFE), vinylidene ﬂuoride (VDF) polymers | Packaging for Pet food, bakery, FOH fried foods
1
2
3
4
Impart Improved Barrier

## Slide 26: Selected Sources of PFAS Tertiary Packaging
Primary Packaging | Tertiary Packaging | Ingredients | Production Environment
  Packaging containing PFAS can come in contact with and then contaminate other packaging that has direct contact with food
  Migration into food can occur through secondary packaging such as labels, coatings, and cartons into food
  Handling of secondary packaging and then food in second-stage BOH/Production environments can contaminate food
1
2
3
4

## Slide 27: Selected Sources of PFAS Ingredients
Primary Packaging | Tertiary Packaging | Ingredients | Production Environment
  Reusable packaging for bulk ingredient transport
    Includes totes, bags, liners, barrels, and bins
    Contamination of reusable totes occurs from prior use of PFAS contaminated ingredients
    Abrasion increases surface area and sites for subsequent migration
    Reuse increases migration due to contact time
  Single-use packaging for bulk ingredient transport
    Totes, bags, liners, barrels, and bins
1
2
3
4

## Slide 28: Selected Sources of PFAS Production
Primary Packaging | Tertiary Packaging | Ingredients | Production Environment
  Equipment used to form packaging
  • Cartoners, labelers, conveyors, thermoformers, unnesters, unscramblers inhibit sticking and make production line move smoother/faster.
  Production equipment used in food processing
  • Extruders, ingredient conveyance systems, hoppers, mixers
  • PTFE (Teflon-Polytetrafluoroethylene) is use for food processing equipment
  Water and CIP cleaning agents
1
2
3
4

## Slide 29: Industry Response has been Fragmented with Drop-in Solutions

## Slide 30: Roadblocks hinder many Drop In Solutions
For many options, there are unintended consequences and/or regrettable alternatives in switching to the still approved SCPFAS
Release Agent Alternatives
  Forming Polymers Alternatives
  Improved Barrier Alternatives
  Improved Barrier Alternatives

## Slide 31: Roadblocks hinder many Drop In Solutions
Release Agent Alternatives
Silicone resins and elastomers as release agents
CAS 7473-98-5, 155419-56-0, 2855-27-8, 102782-94-5, 917773-10-5
Release Agent Alternatives
  Forming Polymers Alternatives
  Improved Barrier Alternatives
  Improved Barrier Alternatives

## Slide 32: Roadblocks hinder many Drop In Solutions
Forming Polymers Alternatives
Alternatives to polymers have a host of chemicals of concern beyond PFAs
Biodegradable alternatives are very problematic
Release Agent Alternatives
  Forming Polymers Alternatives
  Improved Barrier Alternatives
  Improved Barrier Alternatives

## Slide 33: Roadblocks hinder many Drop In Solutions
  Improved Barrier Alternatives
Water barriers - alkyl succinic anhydride (ASA), styrene acrylic emulsion (SAE), alkyl ketene dimer (AKD) and rosin cannot be produced in sufficient volumes and are cost prohibitive now
Biopolymer PTF and synthetic polymer of PEN is promising
Release Agent Alternatives
  Forming Polymers Alternatives
  Improved Barrier Alternatives
  Improved Barrier Alternatives

## Slide 34: Roadblocks hinder many Drop In Solutions
Impart Grease / Oil Resistance Alternatives
Increased density with cellulose, carbon nanofibers, starch coatings during calendaring results in 20-30% slower production
Waxes or Polymer atomization, finishes, coatings may interfere with recycling
Removable and non-removeable plastic liners are not recyclable w/o SDO
Release Agent Alternatives
  Forming Polymers Alternatives
  Improved Barrier Alternatives
  Improved Barrier Alternatives

## Slide 35: Despite Industry efforts, PFAS is Still a Concern
Regrettable substitutions exist
Hiding behind FDA compliance is not protection
Hodge-podge of local and retailer bans
  Industry experts know that substitutions may be regrettable
  This is a costly, and time-consuming game of whack-a-mole
  Data was hidden from FDA
  GRAS status is dubious
  Delayed action continues
  Reliance on voluntary abandonments
Shape-shifting supply chain
Extensive incoming inspection is costly and is not in alignment
  Snapshot do not protect brands or
  consumers

## Slide 36: Despite Industry efforts, PFAS is Still a Concern
Value
Chain

## Slide 37: The Value Chain provides the opportunity to Future Proof Packaging
  Future Proof
  Packaging Value Chain
  Future Proof
  Packaging Value Chain

## Slide 38: Value Chain provides the opportunity to…
Future Proof Packaging
Proactively Plan for the Future - Avoid kicking the can down the road with regrettable substitutions
Build a more valued safety-focused relationship with regulatory agencies
Build/rebuild Trust in all entities of the packaging value chain
Align vs Entrap value chain partners
Future-Proofed Packaging Value Chain
  Future Proof
  Packaging Value Chain
  Future Proof
  Packaging Value Chain

## Slide 39: Case Studies

## Slide 40: Future Proof Packaging Approach Case Studies
    Reduce oil in contact with packaging via a systems approach using one or all of these solutions
    Reformulate fries to
        Enhanced PME-based oil resistance so that less oil is adsorbed
    BOH Processing to
    Adsorb oil prior to FOH packaging with diatomaceous earth or food grade clays
    Use a 2-phase system in which oil is drained more extensively at a station before final FOH packaging
    Non-PFAS plastic (reusable) packaging
    Package redesign to
    Employ a removeable plastic liner within FOH cartons
    FOH cartons with a sealed low point with an adsorbent substance
    FOH cartons dusted with an adsorbent substance
    PFAS sensors on packaging for value chain use
System solutions to replace for oil and grease resistance need in FOH QSR french fry cartons

## Slide 41: Future Proof Packaging Approach Case Studies
1. Advance Barrier technology from 1990s into 2020s
            Provide barrier with enhanced polymer technology in the form of PTF, PEF, or PEN
            Nanoclays to increase tortuosity
            Barrier layers of EVOH, SiOx
            Waxes – but this interferes with recycling
          2. Flip the barrier
      Food contact packaging with minimal barrier
      Provide secondary packaging with enhanced barrier
3. Reduce what needs to be controlled
      Combine secondary and primary packaging investment for overall less packaging to monitor
4. Implement Intelligent packaging
      PFAS sensors on packaging for value chain of custody
Reduce need for a high barrier in direct product contact via a systems approach using one or all of these solutions:

## Slide 42: Future Proof Packaging Approach Case Studies
    Reduce PFAS from contaminated water and feed in all seafood
    Align with other stakeholders and take shared responsibility
    This is instead of – “whew, the pressure of off packaging PFAS is everywhere!”
    Work to define sources and then mitigate those sources
    Engage seafood workers in re-engaging to earn a living in working on PFAS-free fishery development
    Clean-up water
    Engage to clean-up fisheries at issue so people can earn a sustainable living and sell safe seafood
    Manage knowledge
    Link solutions with packaging that communicates “products with no PFAS”
    Define what is needed to provide assurances of “no PFAS”

## Slide 43: Key Takeaways
PFAS regulations are creating stress
PFAS sources in food are from production, processing and packaging
Future Proof Packaging is needed to avoid the pitfalls of a fragmented approach
1
Industry has worked hard with a fragmented approach and alternatives to PFAS face roadblocks
2
3
4

## Slide 44: Q&A Session
Please submit your questions in the GoToWebinar control panel

## Slide 45: Thank you
Walter Brandl
walter.brandl@mxns.com
Regional Director of Chemistry
Mérieux NutriSciences
Dr. Claire Sand
Founder & Owner Packaging Technology & Research
Adjunct Professor, Michigan State University and CalPoly
Reach out to
connect for
a virtual coffee